## Slide 1: CEPC HCAL Readout Electronics

## Slide 2: Content
Background
  CEPC Calorimeters
  CEPC HCAL
  USTC SDHCAL
  SDHCAL Readout ASIC
Design of the Test-Board
  Introduction of Microroc
  Design of the Stage1 Test-Board
  Progress
  Problem
Future Work
  Design a Read-out Array
  Prototype Machine

## Slide 3: Content
Background
  CEPC Calorimeters
  CEPC HCAL
  USTC SDHCAL
  SDHCAL Readout ASIC
Design of the Test-Board
  Introduction of Readout ASIC
  Design of the Stage1 Test-Board
  Progress
  Problem
Future Work
  Design a Read-out Array
  Prototype Machine

## Slide 4: CEPC Calorimeters
Key Calorimeters
  Electromagnetic calorimeter (ECAL)
  Hadron calorimeter (HCAL)
Designed for precise energy measurements of electrons, photons, taus and hadronic jets.
Basic resolution requirements
  ECAL: 16%/√(𝐸(𝐺𝑒𝑉))
  HCAL: 50%/√(𝐸(𝐺𝑒𝑉)).
To achieve these, a Particle Algorithm oriented calorimetry system is being considered as the baseline design.

## Slide 5: CEPC Calorimeters
Particle Flow Algorithm (PFA)
  Charged particles –>tracker
  Photons – >electromagnetic calorimeter
  Neutral hadrons –> hadronic calorimeter
  Approximately 72% of the jet energy is measured
Both ECAL and HCAL are high granularity

## Slide 6: CEPC HCAL
HCAL
  A high-granularity HCAL plays an essential role in CEPC. It allows separation of energy deposits from charged and neutral hadrons. The measurement accuracy of the neutral hadrons is the leading contribution to the jet energy resolution for jets with energy up to 100GeV.
  The HCAL is a sampling calorimeter with steel as the absorber and scintillator tiles or gaseous devices with embedded electronics.

## Slide 7: CEPC HCAL
HCAL Detector Options
HCAL
AHCAL
DHCAL
SDHCAL
Scintillator + SiPM + SPIROC(ASIC), 8148channels,1m3
Analog Hadron Calorimeters(AHCAL).
High power consumption, expensive readout electronics
GEM/RPC/Micromegas + DCAL(ASIC), chn/m3
A hadron calorimeter with only one threshold readout is called a Digital Hadron Calorimeter (DHCAL).
Simple, but poor accuracy. Hard to satisfy PFA
GEM/RPC/Micromegas + HARDROC(ASIC), chn/m3
A more general calorimeter with multi-threshold readout (e.g. 3 thresholds) is therefore also considered, a so-called Semi-Digital Hadron Calorimeter (SDHCAL).
A balanced choice for CEPC HCAL
Absorber: steel
Active layers: Gaseous detector

## Slide 8: USTC SDHCAL
Architectural of the SDHCAL
A scheme of the ASU used to readout 1m2 detector
Absorber(Fe, W)
Sensor(RPC,MM,GEMTHGEM)
PCB

## Slide 9: USTC SDHCAL
Approximatively, 95% Energy included longitudinal length:
L(95%)=[0.56*ln(E/GeV)+2.33] λI
E=100GeV, L(95%)=4.9 λI =82.2cm(Fe)=48.7cm(W)=75.1cm(Cu)
The energy resolution of HCAL will be improved by using more sampling layers, but it won’t work any more when d<2cm (for Fe) .
95% Energy included transverse radius: ~30cm for 50GeV π±, 99% hits in 70cm× 70cm.

## Slide 10: SDHCAL Readout ASIC
Hardroc
  HAdronic Rpc Detector ReadOut Chip
  Dynamic range: 10fC ~ 10pC
  3 DAC for threshold
Microroc

## Slide 11: Content
Background
  CEPC Calorimeters
  CEPC HCAL
  USTC SDHCAL
  SDHCAL Readout ASIC
Design of the Test-Board
  Introduction of Microroc
  Design of the Stage1 Test-Board
  Progress
  Problem
Future Work
  Design a Read-out Array
  Prototype Machine